## Slide 1
START
INITIALIZE
Geometry & Material Properties
Boundary Conditions
Boundary Values
Initial Carrier Distribution
Calculate Net Charge
Solve Poisson’s Equation
Calculate Current Density
(Finite Difference/Scharfatter-Gummel)
Calculate Divergence of Current Density
& Update Carrier Distribution
(Implicit or Explicit Time stepping)
Check for Stopping Criteria
Stop Simulation
Yes
Output Results
No
(High Charge density)
No
(Low Charge density)